## Slide 1: Maker’s university – by intel’s makers community class 4 – Remote access
Gil Tal.
Jan 2020

## Slide 3: Class 4 agenda:
Control and communication over the air
  Wi-Fi
  Bluetooth
Wi-Fi basics
Webserver
Micro DNS
ESP-Now protocol
Useful web services and protocols
IOT
Bluetooth
OTA (Over The Air update)

## Slide 4: Wi-fi basics
Wi-Fi basics:
  Family of wireless networking technologies
  IEEE 802.11 family of standards
  Used for local area networking of devices and Internet access
  20-150 meters range
  Standard defines 16 channels for communication
    Enables multiple access points at the same physical location

## Slide 5: Wi-fi basics: AP and sta
AP – Access point
  Enable the creation of a local Wi-Fi network
  We connect to an access point
  With or without access to the internet
  Uses a specific channel which can be modified while operating
  Has limitation for number of connected devices
  Has a name and an optional password
  Can use an encrypted communication protocol
STA – Station
  An end point device
  Connects to an AP
  While searching for an AP needs to try different channels until found
AP
End Point device

## Slide 6: Wi-fi basics: our esp32
Runs full network stack
Can function as:
  AP
    By default enables up to 4 users
  STA
  Both*

## Slide 7: webserver
Web pages are hosted on a webserver
  Most commonly written in HTML5 + JAVA script
  There are various HTML5 emulators out there
Has a specific IP address (192.168.14.1 for example)
Is a passive device
We need a browser to access it
  Browser is executing the HTML5 code
  The communication protocol is HTTP
There are large number of hosting providers
IP address can be replaced by a name
  DNS server translates the name to the specific IP address
ESP32 can run a webserver! 

## Slide 8: Webserver – what can we do with it
Have a nice GUI to communicate with the ESP32 using a browser
Control IOs
Get information from our ESP32
  Such as temperature, humidity depending on what we connected
Send data to the ESP32
  Files
  Raw data

## Slide 9: Webserver – work flow
We need to initialize:
  WiFi
  Webserver
Prepare the HTML for the pages
Handle the client which interacts with the browser
Process the incoming data from the browser to perform actions on the ESP

## Slide 10: Webserver – Init code

## Slide 11: Webserver – INIT code

## Slide 12: Webserver – html data

## Slide 13: How does it looks…

## Slide 14: Webserver – handle the client

## Slide 15: Webserver – processing incoming data

## Slide 16: Multicast DNS
Domain Name System
MDNS – Is a zero-configuration service
Enables usage of names instead of IP address
Our ESP32 runs Multicast DNS (MDNS)
Windows and Apple devices can work with MDNS
Sadly Android does not 
Usage:
  http://esp32.local/
  No MDNS support - http://192.168.14.1/ (just an example IP)

## Slide 17: No mdns on Android so… (buy an iPhone  or)

## Slide 18
Protocol developed by Espressif
Enables multiple devices to communicate without using Wi-Fi
Low-power 2.4GHz wireless connectivity
Encrypted and unencrypted unicast communication
Up to 250-byte payload can be carried
10 encrypted peers at the most (STA mode), 6 for SoftAP or STA + SoftAP

## Slide 19: Esp-now
Works with MAC address
Need to know the our MAC and the Peer’s
Initialize the protocol
Register callback functions for send and receive
Register peers
Upon sending the send function will be called:
  With status
  With the MAC of the targeted peer
Upon receiving the receive function will be called:
  With the MAC of the sender
  With the received data

## Slide 20: Useful web services
NTP - Network Time Protocol
Weather data
Feeds (News, Sports and more)
GEO location