## Slide 1: Maker’s university – by intel’s makers community
Gil Tal.
Jan 2019

## Slide 3: Expectations:
It is the first time – so I will be experimenting along with you all
Not everything is ready
We are creating something new!
I need help with infrastructure which is still work in progress
You can choose to be the instructor for the next classes , at Intel or anywhere you choose
Most of the work will be done at your own free time
You are expected to complete missing knowledge you might have
C\C++ good knowledge is required

## Slide 4: targets:
To take us a step up as an engineers
To expose us to new opportunities \ possibilities \capabilities
To enable us to execute small to medium projects – end to end
To train us as instructors to run similar course at schools\universities – to better expose Intel
To grow this new thing we are starting

## Slide 5: So what has changed?

## Slide 6: Course agenda:
What does it mean being a maker?
What are we going to learn?
What is the Arduino platform?
What is a micro controller?
What can I do with a micro controller?
Basic communication protocols
Our general maker’s platform
Available accessories/peripherals/devices
Our first project
Board design
Debug capabilities: logic analyzer, scope and maybe JTAG debugger
3D printing with design

## Slide 7: Being a maker, what does it mean?
A maker is an electronic biased hobbyist
You need to have basic and up SW and HW capabilities
And foremost you need passion 
Makers these days have huge possibilities very easy to reach
Arduino for example is a very reachable and easy to use maker’s platform
Makers today can easily:
  Built their own drones
  Do home automation
  Build complex gadgets
  Build a robot
  Imagination will be your only limit (almost )

## Slide 8: What are going to learn?
Code and run various examples and exercises on Intel’s makers platform
Pick your own project*
Code it …
Design an electric board, manufacture it, assemble and test it
Learn how to design a 3D case or parts and print it with our 3D printers
Tie it all together and have fun 

## Slide 9: What makes for a good maker platform?
A chip micro controller
I/Os - Input and Output pins (Digital and analog)
Easy programmability
Capability to easily connect external accessories/peripherals/devices
IDE - Integrated Development Environment
Bonuses:
  File system support
  Wi-Fi
  Bluetooth
  PWM - Pulse-Width Modulation
  Wide and active community

## Slide 10: The Arduino makers platform – how it all started…
The Arduino project was started at the Interaction Design Institute Ivrea (IDII) in Ivrea, Italy
In 2003 Hernando Barragán created the development platform Wiring as a Master's thesis project at IDII – Which was used as the basis for the Arduino platform
Under the supervision of Massimo Banzi and Casey Reas. Casey Reas is known for co-creating, with Ben Fry, the Processing development platform
The project goal was to create simple, low cost tools for creating digital projects by non-engineers!
The initial Arduino core team consisted of Massimo Banzi, David Cuartielles, Tom Igoe, Gianluca Martino, and David Mellis, but Barragán was not invited to participate
Millions of Arduino boards are in use around the world!

## Slide 11: Arduino
As said Arduino was born at the Ivrea Interaction Design Institute as an easy tool for fast prototyping, aimed at students without a background in electronics and programming. As soon as it reached a wider community, the Arduino board started changing to adapt to new needs and challenges, differentiating its offer from simple 8-bit boards to products for IoT applications, wearable, 3D printing, and embedded environments. All Arduino boards are completely open-source, empowering users to build them independently and eventually adapt them to their particular needs. The software, too, is open-source, and it is growing through the contributions of users worldwide.

## Slide 12: The Arduino makers platform
Arduino platform offers:
  A variety of cheap boards
  A simple to use IDE that supports C\C++
  Open source
  Huge community
  Training and example projects are all over the web and within the IDE!
  Visual Micro provides a plug-in for visual studio to provide the ultimate IDE
Other micro processors platforms were built to use the Arduino IDE and offers much better capabilities at a very low cost!
  Such as Espressif System’s ESP8266 and ESP32

## Slide 13: Arduino options
Board Name | CPU | Clock | SRAM | FLASH | EEPROM | UART | PWM | Analog Out | DAC Bits | Digital | Analog In | ADC Bits | VCC | I2C | CAN | SPI | I2S | Touch Sensors | WiFi | Bluetooth | Board price
Arduino Due | SAM3X8E - 32 bit | 84MHz | 96kb | 512kb | N/A | 4 | 12 | 2 | 12 | 70 | 12 | 12 | 3.3V | 2 | 1 | 1 |  |  |  |  | 11$
Arduino Zero | ATmega328 - 32 bit | 48MHz | 32k | 256k | N/A | 2 | 18 | 1 | 10 | 20 | 6 | 12 | 3.3V | 1 |  |  |  |  |  |  | 10$
Uno (R3) | ATmega328 - 8 bit | 16MHz | 2k | 32k | 1k | 1 | 6 | N/A | N/A | 14 | 6 | 10 | 5V | 1 |  |  |  |  |  |  | 5$
Arduino Mega 2560 | ATmega2560 - 8 bit | 16MHz | 8k | 256k | 4k | 4 | 14 | N/A | N/A | 54 | 16 | 10 | 5V | 1 |  |  |  |  |  |  | 
Arduino Nano 3.0 | ATmega328 - 8 bit | 16MHz | 2k | 32k | 1k | 1 | 6 | N/A | N/A | 14 | 8 | 10 | 5 | 1 |  |  |  |  |  |  | 
Arduino Mini | ATmega328 - 8 bit | 16MHz | 2k | 32k | 1k | 1 | 6 | N/A | N/A | 14 | 8 | 10 | 5 | 1 |  |  |  |  |  |  | 
Arduino Micro | ATmega32u4 - 8 bit | 16MHz | 2.5k | 32k | 1k | 1 | 7 | N/A | N/A | 25 | 12 | 10 | 5V | 1 |  |  |  |  |  |  | 3$
Arduino Nano 33 BLE Sense | UBLOX NINA B306 | 64MHz | 256KB | 1MB |  | 1 |  |  |  | 8 | 13 |  | 3.3V | 1 |  | 1 |  |  | Yes | Yes | 30$
ESP8266 | Tensilica LX106 32 bit | 160MHz | 80K | 4MB | 4K | 1 | SW | N/A |  | 9 | 1 | 10 | 3.3V | 1 |  | 1 |  | No | Yes | No | 3$
ESP32 | Tensilica Dual LX6 32 bit With Thread-X OS | 240MHz | 512K | 4MB | 4K | 2 | 1/16 | 2 | 12 | 36 | 18 | 12 | 3.3V | 1 | 1 | 2 | 2 | Yes | Yes | Yes | 4-5$

## Slide 14: What is a micro controller?
Basically it is a system on a chip – meaning …
It has almost all we need to run a computing system in a single chip:
  CPU
  Dynamic memory
  Non volatile memory
  Communication ports
  I/O ports
  The rest depends on the complexity of the micro controller

## Slide 15: General Block diagram

## Slide 16: Esp32 block diagram

## Slide 17: More about the esp32
Dual core with full cache coherency
Support true multi threading and function bounding to specific CPU
512KB of SRAM
4MB of flash memory
ESP class gives access to:
  Heap size (available RAM at any moment)
  EEPROM (4KB)
  Control over CPU frequency
  Deep sleep
  CPU 64 bit counter
  Flash memory control functions
  More…
Running FreeRTOS operating system which can be utilized or ignored

## Slide 18: What can I do with a micro controller?
Many electric devices such as laundry machines, refrigerators, micro waves are powered by micro controllers
Advanced toys such as drones, robots and much more …
Home automation
IOT
Simple to highly advanced digital projects

## Slide 19: Cool examples

## Slide 20: Cool examples

## Slide 21: Cool examples

## Slide 22: accessories/peripherals/devices - Properties
Communication protocol voltage level
Voltage supply
Power consumption
Band Width
SW Driver
Timing specifications
  Setup, hold and the alike
  Max frequency (when relevant)
Protocol
  Sync – meaning using clock (limited frequency) or sync signals
  A-Sync
  Data assurance\protection using (parity, ECC, CRC etc.)

## Slide 23: What is a device driver?
A set of SW functions to enable easy operation and communication of/with a device
Good driver:
  Has easy to use and understand API (Application Programming Interface)
  Can be easily ported to similar devices

## Slide 24: Basic communication protocols
Devices can be connected physically by copper wires or over the air (Wi-Fi, Bluetooth, RF, WEB)
There are various communication protocols, some are standard and some are unique
Simple protocols are: (Low to medium speed and bandwidth)
  I2C (Two wires – data and clock) (100 or 400 KHz) – can serve many devices concurrently
  UART (RS232) (9600 up to 115200 bps) – only one device per interface
  SPI - Serial Peripheral Interface (1 – 100 MHz, data width 1 up to 8 bit) - – can serve many devices concurrently
  RF (LoRa and more)
Advanced protocols (Medium to very high speed and bandwidth)
  Bluetooth
  Wi-Fi: Ethernet – TFTP, UDP,WEB
  PCIe (up to 16GHz 16 bit width)
  USB2\3 (up to 10GHz)
  Thunderbolt (up to 40GHz)

## Slide 25: End to end example

## Slide 26: RS232 - UART
Was born in 1960
In the basic mode uses two signals: RX and TX (Receive and Transmit)
Works at speeds from 4800 (bits per second) up to 921000 (usually 115200 is being used)
Works at various voltages (although the standard is +/- 12V)
Used by most of the micro controllers as the main communication port

## Slide 27: Configuration of RS232
Both sides must be set with the same configuration and voltage level*
  BAUD rate (speed – 9600, 115200 or any other supported speed)
  Use parity bit or not (in most cases not used)
  Number of stop bits: 1 or 2 (in most cases 1 stop bit)

## Slide 28: Our general platform…

## Slide 29: Available accessories/peripherals/devices
Sensors: Motion, distance, temperature, color, light, smoke, gas, humidity and more
Input: Potentiometers, simple on\off buttons, touch devices, analog joy sticks and more
Displays: LCD and LED matrix
Storage: Flash memory, SD cards, I2C EEPROM
Servo and DC motors
Physical and solid state relays
Infrared transmitters and receivers
RF based I/O
Battery chargers
RTC (Real time clock)
GPS, accelerometers
3G modem with SIM card supporting calls and SMS send\receive
Finger print sensor
Just search the web and you will be amazed by what is out there!

## Slide 30: Getting started …

## Slide 31: Building a project
Define the project
  System requirements specifications
  Block diagram
  Computing needs
  Accessories\Peripherals\Devices needed
  Budget
Choosing the right micro controller and board
Choosing the right Accessories\Peripherals\Devices
  Sometimes same devices uses different protocols
  We need to make sure the voltage levels are compatible
  Communication channel are compatible with our MC and has no BW limitations
We need a PC usually running widows on which:
  We install the Arduino IDE
  Connecting the micro controller board using a USB port

## Slide 32: Basic code in Arduino
void setup() {
// put your setup code here, to run once:
}
void loop() {
// put your main code here, to run repeatedly:
}

## Slide 33: Board design process
Block diagram
Parts selection
Schematic
DRC + Net List check
Board definitions
  Number of layers
  Conductor’s width (Net classes)
Placement
Routing
DRC + placement check
Generate production files
Send to production
Assembly
Test al lab 

## Slide 34: List of Projects
Led on\off using simple physical button
LCD simple drawing
WEB based Led on\off (Local and over the cloud)
Bluetooth heart rate monitor
Step motor operation
Advanced LCD application
File System
OTA – over the air SW update