## Slide 1: Maker’s university – by intel’s makers community class 7 – getting started with the drone 
Gil Tal.
Mar 2020

## Slide 3: Class 7 agenda:
What do we need to run a drone?
Basic knowledge we might be missing
Block diagram

## Slide 4: What do we need?
Engines (motors) with rotors
Two ways LoRa Receiver\Transmitter for communication and control
GPS
Barometer for altitude
Gyro and Accelerometer
LiPo battery
Micro Controller with proper interfaces
Small removeable LCD for debug

## Slide 5: Engines with rotors
Brushless servo DC motor (high current 16-30A)
ESC (electronic speed control) is an electronic circuit that controls and regulates the speed of an electric motor
KV is Max RPM rating of the motor
ESC has 8 pins:
ESC
Power
Servo
Connector
(Via PWM)
From LiPo Battery

## Slide 6: Communication
LoRa – Long range two ways LoRa Receiver\Transmitter
3-5 KM range
433/868/915 MHz
Uses UART protocol to communicate with the MCU
3.3V
Driver available for Ardunio

## Slide 7: GPS
Uses UART protocol to communicate with MCU
3.3V
Driver available for Arduino

## Slide 8: Barometer (BM280)
Uses I2C protocol to communicate with MCU
3.3V
Driver available for Arduino
Measures:
  Humidity
  Temperature
  Pressure (For Altitude) – ~1m accuracy

## Slide 9: 6050 MPU
3 Axis analog gyro sensors + 3 Axis Accelerometer
Uses I2C protocol to communicate with MCU
3.3V
Driver available for Arduino

## Slide 10: 1.3” MINI LCD for debug
Uses SPI protocol to communicate with MCU
3.3V
Driver available for Arduino

## Slide 11: Our MCU – ESP32 Dev Kit

## Slide 12: Block diagram
ESP32
Dev Kit
LiPo
Battery – XT60
Connector
GPS
BM280
6050
LoRa
Connectors for ESCs
PWM
UART
UART
I2C
LCD
SPI
5V
GND