## Slide 1: Maker’s university – by intel’s makers community class 6 – board design
Gil Tal.
Feb 2020

## Slide 3: Class 6 agenda:
Basics (very basics) electronics
What is a PCB?
Board producing process
Schematic
Design rules
Board
Placement
Routing
Production
Board power on and debug

## Slide 4: OHM law
V = R*I (URI)

## Slide 5: Basic components
A resistor is a passive two-terminal electrical component that implements electrical resistance as a circuit element.
Basically turns electrical energy into heat.
Measure unit: ohm
Usages: Limit current, drop voltage level, Pull up/down floating signals
A capacitor is a device that stores electrical energy in an electric field. It is a passive electronic component with two terminals.
Measure unit: Farad
Usages: Handle power supply surge, very fast absorption of electrical energy (also fast discharge), along with a resistor a simple reset at power on

## Slide 6
A diode is a two-terminal electronic component that conducts current primarily in one direction (asymmetric conductance); it has low (ideally zero) resistance in one direction, and high (ideally infinite) resistance in the other.
A transistor is a semiconductor device used to amplify or switch electronic signals and electrical power

## Slide 7
Open drain buffer: Either drives ground or float the output
A pull up resistor is needed to drive logic 1
Bi-Directional I/O
Tri state buffer:

## Slide 8: PCD
Printed circuit board
Mechanically supports and electrically connects electrical or electronic components
Using conductive tracks, pads and vias
May be composed from few layers of copper laminated onto and/or between layers of a non-conductive substrate

## Slide 9: PCD - Structure
Standard thickness 1.6mm
Suggested trace width for cheap PCBs 5-6 mil (check with manufacturer)
Via connects traces between different layers
Pads are used for soldering devices
Via
Via
Via
Trace
Pads

## Slide 10: Board producing process
Block diagram
Devices
Pick up
Schematic
ERC +
Netlist
Board
creation
Placement
Routing
DRC
Generate
Production
Files
Send board
To production
Purchase
components
Assembly
Power On

Set rules
For routing

## Slide 11: Schematic – Step 1
Draw a block diagram

## Slide 12: Schematic – Step 2
Decide which components to use – pay attention to:
  I/O Voltage
  What types of I/Os does it have
  Power supply voltage
  Type of packages (Next slide)
  Type of I/Os (specially open drain needs attention)
  Does it use an output enable? If yes check polarity
  Does it need reset? If yes check polarity
  Does it need a pull up for some of its signals? (interrupts for example)
  Does it have a sample at reset pins?
  Check if it has I/Os that functions differently under reset?

## Slide 13: Different types of packages
Through hole (TH)
SMT (Surface Mount)
BGA (Ball Grid Array)

## Slide 14: Schematic – Rules and caveats
Two outputs cannot be connected to each other
  It can happen without paying attention
Do not leave a floating signals or I/Os
I/Os voltage level must be suitable
  Some devices has I/Os that can tolerate high voltage
Special I/Os needs special attention:
  Open drain must have pull ups
  I/Os which have output enable must have a pull up/down
  Sample at reset I/Os
Most component need a capacitor\s placed near the power supply
I2C devices addresses needs coordination

## Slide 15: Schematic – Step 3
Create a new project in Eagle
  Draw your schematic
  Components needed must be in the library

## Slide 16: Board – Step 1
In Eagle generate the board

## Slide 17: Board – Step 2
Set the physical size of the board
Set the number of layers (default is 2, we will not use more than 2)
Set the net classes: (Edit->Net classes)
  Power
  Regular signals (default)
  Custom if needed
Set the project’s general settings:
  Edit->Design Rules
    Clearance: 6 mil
    Sizes
    Supply

## Slide 18: Board – Step 3
Placement:
Locate your components on the physical board
Try to keep them all on the components side (upper layer)
Set drills for mounting
Do a placement physical check
  Print the board in 1:1 ratio
Create planes if needed
  For power supply plane, set the thermal attribute off
On
Off

## Slide 19: Board – Step 4
Routing:
Route (use the auto router)
  Complete un routed signals
Run an ERC check
Fix whatever needed
Add text
Generate the production file
Send to production and prayer 